## Slide 1: Evaluating OpenMP Affinity on the POWER8 Architecture
Swaroop Pophale and Oscar Hernandez
October 6th, 2016

## Slide 2: Outline
Motivation
Background
Experiment
Observations
Conclusion

## Slide 3: Motivation
In the near future DOE leadership class systems will consist of OpenPOWER compute nodes.
Understand working with OpenMP 4.0 on P8 is crucial
Observe variability in performance of applications
  this variability gives a lower bound and upper bound of expected performance
  document hardware counters that may indicate a problem with affinity/data placement

## Slide 4: Background
Memory Placement
  First touch
    default on many systems
    first access to data is representative of the application ́s data accesses throughout the life of the application
    Data is marked to be placed on the node of the CPU that accesses it.
  Next Touch
    Difficult to implement correctly
    Data is marked to be placed on the node of the next CPU that accesses it.

## Slide 5: Background
Affinity in OpenMP 4.5
  OMP_PROC_BIND ICV / proc_bind clause
    set the thread affinity policy
    Valid values: true, false, close, spread and master
  OMP_PLACES
    placement on a given hardware.
    Valid values: thread, core, socket, or numeric ( generally maps to hardware thread)
      “The meaning of the numbers and how the numbering is done are implementation defined”
Data placement and thread binding are orthogonal, but together have a profound effect on application performance
Notes: Intervals can be specified using the <lower- bound> : <length> : <stride> notation to represent the following list of numbers: “<lower-bound>, <lower-bound> + <stride>, ..., <lower-bound> + (<length>- 1)*<stride>.”

## Slide 6: Background
Power8
Fig 1: Machine Architecture
Fig 2: Memory Subsystem

## Slide 7: Background
Each processor contains two chiplets of 3, 5 or 6 cores.
Cache hirarchy
  512 KB SRAM L2 caches per core,
  96 MB eDRAM shared L3 and
  Off chip L4 cache 128 MB eDRAM space
Non-Uniform Cache Architecture (NUCA) Cache Policy within the chip
  allows a shared L3 cache with scalable bandwidth and latency
  migration of most used cache lines to the local L2 cache and then to the local L1 cache

## Slide 8: Background
Power8 Hardware Counters
  CPI Stack accounts for stalled, waiting to complete, thread blocked, completion table empty, completion and other miscellaneous cycles.
  Newly added : Stall cycles due to Dcache Misses
    Stall by Data Cache (L1) misses
    Stall by Dcache miss which resolved in L2/L3
    Stall due to cache miss due to L2 L3 conflict
    Stall due to cache miss due to no L2 L3 conflict
    Stall due to cache miss resolving missed the L3
    GCT empty by branch mispredict + IC miss
    Stall by Dcache miss which resolved on chip
    Stall by Dcache miss which resolved from remote chip
    Stall by L1 reloads from distant interventions and memory

## Slide 9: Experimentation
  Experimental System:
    Dual socket POWER8 system with 256GB of main memory
    Four POWER8 chiplets, that map to four NUMA nodes
    Total of 20 cores over two sockets (10 each), 8 hardware threads per core
  We define the OpenMP Affinity tuple as a combination of (OMP_PROC_BIND, OMP_PLACES)
    Examples of setup: OMP_NUM_THREADS = 10, OMP_PROC_BIND = master
    OMP_PLACES = threads OMP_PLACES = cores OMP_PLACES = sockets
Socket 1
Socket 2
Socket 1
Socket 2
Socket 1
Socket 2

## Slide 10: Experimentation
      To efficiently use NUMA resources
      OMP_PROC_BIND = master, OMP_PLACES = 0:8:10 and OMP_NUM_THREADS = 10
      Note:
        Non-portable way to specify placement of threads
        Spread and close could be used, but
          Both schemes distribute threads in a round-robin fashion
          Determination of whether the affinity request can be fulfilled is implementation defined.
Socket 1
Socket 2
Occupied Core
Free Core
Notes: OMP_NUM_THREADS=10
OMP_PROC_BIND=master
OMP_PLACES=cores
MAPPING
Thread=0, CPUID=0
Thread=1, CPUID=1
Thread=2, CPUID=2
Thread=3, CPUID=3
Thread=4, CPUID=4
Thread=5, CPUID=5
Thread=6, CPUID=6
Thread=7, CPUID=7
Thread=8, CPUID=7
Thread=9, CPUID=0
OMP_NUM_THREADS=10
OMP_PROC_BIND=master
OMP_PLACES=sockets
MAPPING
Thread=0, CPUID=18
Thread=1, CPUID=26
Thread=2, CPUID=33
Thread=3, CPUID=5
Thread=4, CPUID=14
Thread=5, CPUID=15
Thread=6, CPUID=6
Thread=7, CPUID=34
Thread=8, CPUID=19
Thread=9, CPUID=8

## Slide 11: Experimentation
Jacobi Kernel
!$omp parallel do private(xx,yy)
do j = 1,m
do i = 1,n
xx = -1.0 + dx * dble(i-1)
yy = -1.0 + dy * dble(j-1)
…
…
enddo
enddo
!$omp end parallel
Listing 1: Parallel initialization – data affinity
!$omp parallel num_threads(1)
do j = 1,m
do i = 1,n
xx = -1.0 + dx * dble(i-1)
yy = -1.0 + dy * dble(j-1)
…
…
enddo
enddo
!$omp end parallel
Listing 2: Sequential initialization – no data affinity

## Slide 12: Experimentation
Jacobi Kernel
!$omp do private(resid) reduction(+:error)
do j = 2,m-1
do i = 2,n-1
* Evaluate residual
resid = (ax*(uold(i-1,j) + uold(i+1,j))
& + ay*(uold(i,j-1) + uold(i,j+1))
& + b * uold(i,j) - f(i,j))/b
* Update solution
u(i,j) = uold(i,j) - omega * resid
* Accumulate residual error
error = error + resid*resid
end do
enddo
!$omp enddo nowait
!$omp end parallel
Listing 3: Parallel Computation

## Slide 13: Observations
Fig 3: Performance comparison with 20 OpenMP threads

## Slide 14: Observations

## Slide 15: Observations
With the first touch policy
  Thread binding value true, close and master don’t benefit from better data locality as all threads contend for resources of the same NUMA domain

## Slide 16: Conclusion
P8 memory sub-system is complex
Applications must consider the different levels of caches and protocols that govern them
Although all memory is shared NUMA and NUCA latencies have to be considered.
Notes: How thread affinity and data placement affect app on P8
  both settings are orthogonal but are related
  How sensitive an application is to thread affinity
  Cost of NUMA effects
How do we find out if we have a problem with affinity/data placement
What are the hw counters that we need to watch and how they help
These are the only way to specify custom affinity - 1 thread per numa node
MISSING - Missing portable way of defining placement as NUMA, usability, what are the caveats there (too simple)
Future work - What algorithms are affected by affinity (types - compute bound/memory bound etc.)